Clarke Manufacturing Inc. 13388 S. Molalla Forest Rd. Molalla OR. 97038

Part # 11616 BETA (2010-2011) 350/400/450/520 RS/RR (2006-2008)

3.8 Gallon Fuel Tank

Thank you for purchasing a Clarke fuel tank.  The following instructions will help you install this tank on a BETA four stroke motorcycle.  There may be some plastic shavings left in the tank from the manufacturing process.  You can use compressed air to blow out the tank.  You may also want to rinse out the tank using a small amount of fuel before installing it. This tank will fit without any modification on the bike itself, but will require the use of the included front mount bracket. The instructions on the back side of this page will help you to quickly install your new tank

PLEASE SEE THE REVERSE SIDE OF THIS PAGE FOR INSTALLATION INSTRUCTIONS

1.) Begin by removing your old seat, tank, shrouds and petcock assembly.  Drain your old tank in a

well ventilated area.  You will not need the original radiator shrouds.

2.) Install your original petcock assembly into the new tank using the supplied allen head bolts that are included with the new tank.

3.) Take the supplied front mount bracket assembly and unbolt it from the new tank.  Insert your factory front mount bolt and washer down through the center of the bracket and bolt it firmly to the original mounting area on the bike.

4.)  Transfer the forward seat mount stud and the rear center mount hardware from your old tank to the new one.

5)  Place the tank on the frame and push it into position aligning the tank over the rear center mount hole and  front bracket that you just installed on the frame making sure the inserts on the bottom of the tank line up with the holes on the outer ends of the bracket.

6.) Using the supplied screws and washers, loosely bolt the bracket to the underside of the tank.

It is recommended that you use “Blue Lock-Tite” to ensure that the bolts stay in.

7.)  Now bolt down the rear of the tank using your original rear mount bolt.

8.)  Using the supplied aluminum spacers, align the grommets and spacers in the “shroud” area on either side and start the supplied bolts through the grommets and bolt the tank to these locations loosely as well.

9.) Now go back around and tighten the front bracket bolts, the rear center mount and the “shroud” bolts so that the tank is completely mounted and tight.

10.) Hook up fuel line and fill with gas.

11.) Check for leaks.

12.) Re-install the seat and fasten the seat mount bolt securely.

13.) You are now ready for riding. Enjoy your new Clarke tank.