Clarke Manufacturing Inc. 13388 S. Molalla Forest Rd. Molalla OR. 97038

Part # 1394 ATC110/125M 1983-1985

STOCK CAPACITY FUEL TANK

Thank you for purchasing a Clarke fuel tank.  This tank is intended use on the ATC110/125M. There may be some plastic shavings left in the tank from the manufacturing process.  You can use compressed air to blow out the tank.  You may also want to rinse out the tank using a small amount of fuel before installing it.  ** PLEASE NOTE:  On the OEM unit there are holes to bolt the rear of the tank down.  The plastic tank that you have purchased does NOT have a provision to mount in this manner.  DO NOT DRILL ANY HOLES IN THIS TANK.  The seat style on this ATC is sufficient to hold the rear of the tank down.

PLEASE SEE THE REVERSE SIDE OF THIS PAGE FOR INSTALLATION INSTRUCTIONS

1.) Shut off fuel supply, disconnect fuel lines and remove the original tank and petcock hoses.  Drain your old tank in a well ventilated area.

2.) Slide the tank onto the front rubber mounting pucks.  You may need to adjust the tank more forward or back so that you find the best possible fit to your seat.

3.) Now hook up the fuel lines, turn the petcock to the OFF position and fill the tank with gas.

4.) Check for leaks

5.) Re-install the rear fender and seat assembly adjusting fit as necessary with the tank.

6.) You are now ready for riding. Enjoy your new Clarke tank.