Clarke Manufacturing Inc. 13388 S. Molalla Forest Rd. Molalla OR. 97038

Part # 1401 CR250 and CR125 2000-2001

3.1 GALLON FUEL TANK

Thank you for purchasing a Clarke fuel tank.  The following instructions will help you install this tank on a CR250 and CR125 2000-2001 motorcycle.  There may be some plastic shavings left in the tank from the manufacturing process.  You can use compressed air to blow out the tank.  You may also want to rinse out the tank using a small amount of fuel before installing it. The instructions on the back side of this page will help you to quickly install your new tank.

PLEASE SEE THE REVERSE SIDE OF THIS PAGE FOR INSTALLATION INSTRUCTIONS

1.) Begin by removing your old tank, shrouds and petcock.  Drain your old tank in a well ventilated area.

2.) Install your original petcock mount in the new tank.

3.) To provide more clearance, take your radiator clamps and turn them over so that the screws are facing

in toward the radiator itself.

4.) Using the 6mm x 35mm bolt supplied, insert them into the rubber grommet that is in the front of the new tank.  Now slide your stock aluminum spacer into the grommet from the BOTTOM of the mount and

make sure that the bolt is still in place.

5.) Place the tank in the frame and looking underneath the front, align the front of the tank over the mount hole while pushing the tank in place.  Tighten the bolt.

6.) Transfer the rear seat mount stud and the rear strap mount screw to the new tank.

7.) Attach the rubber strap to the rear screw.

8.) Using the original shroud bolts, loosely attach the upper part of the shrouds to their original positions.

9.) Now loosely attach the lower frame mount and radiator mount locations using your original bolts.

10.) Go back and tighten all bolts, hook up fuel line, turn the petcock to the OFF position and fill with gas.

11.) Check for leaks.

12.) Re-install the seat and fasten the seat mount bolts securely.

13.) You are now ready for riding. Enjoy your new Clarke tank.