Clarke Manufacturing Inc. 13388 S. Molalla Forest Rd. Molalla OR. 97038

Part # 11606 HODAKA 125 STOCK REPLICA FUEL TANK

Thank you for purchasing a Clarke fuel tank designed to fit the Hodaka 125 line of motorcycles.  Please note that the Hodaka Badge in the picture is not included, these were purchased from Strictly Hodaka.  There may be some plastic shavings left in the tank from the manufacturing process.  You can use compressed air to blow out the tank.  You may also want to rinse out the tank using a small amount of fuel before installing it. The instructions on the back side of this page will help you to install your new tank properly.  Upon purchase and installation the consumer assumes all liability and is solely responsible for compliance with all local and federal laws.

PLEASE SEE THE REVERSE SIDE OF THIS PAGE FOR INSTALLATION INSTRUCTIONS

1.) Begin by removing the original tank and seat

2.) Drain any remaining fuel from the OEM tank in a well ventilated area and then make sure that

the petcock is turned to “OFF”

3.) Look at the bottom of the new Clarke tank and select which side you need the new petcock to be installed on.  Then using a ¼” drill, carefully drill out the fuel outlet hole in the new tank.

4.)  Using the supplied petcock, o-ring and screws install the Clarke petcock to the new tank and turn the lever to off.

5.) Install the supplied front mounting brackets to the front of the tank using the supplied hex bolts and lock washers.

6.) Take the supplied frame padding and cut it into rectangular usable shapes and double it up on the frame front and back.  You can zip-tie or duct tape these on.

7.)  Slide the Clarke tank on the frame and adjust padding as necessary for a snug fit.  Now align the tank with the factory front mount location.  Using the supplied hex bolts and larger washers bolt the tank down to the front mounts.

8.) Now take the supplied rectangular tank strap and bolt it to the bottom of the tank underneath the frame on both sides.  Put the supplied rubber washers between the tank and the strap using the supplied bolts and lock washers.

9.) Fill the tank and check for leaks. Clarke tanks are pressure tested with air before they are shipped, but this is a necessary precaution.  Make sure the petcock is still in the “OFF” position.

10.) You may now hook up your fuel line back to the carburetor, it is suggested that you use an inline fuel filter between the petcock and the carburetor.

11.) Re-install the seat assembly and make sure all bolts are tight.

12.) You are now ready for riding. Enjoy your new Clarke tank!