Clarke Manufacturing Inc. 13388 S. Molalla Forest Rd. Molalla OR. 97038

Part #1419 TRX400EX ( ALL YEARS )

5.5 GALLON FUEL TANK

Thank you for purchasing a Clarke fuel tank.  This tank is intended for use on a TRX400EX.  There may be some plastic shavings left in the tank from the manufacturing process.  You can use compressed air to blow out the tank.  You may also want to rinse out the tank using a small amount of fuel before installing it.  Please note that for this tank to be mounted properly you will not need to use the existing black side panels.  Most of the additional fuel capacity is achieved by filling in this area with fuel tank and following the original lines of the side panels.

Picture 1.                                      Picture 2.                                    Picture 3.                                 Picture 4.

( Using An End Wrench To Properly Install Rear O-Rings To Mounts )

PLEASE SEE THE REVERSE SIDE OF THIS PAGE FOR INSTALLATION INSTRUCTIONS

1.)  Begin by rinsing out your new tank with a small amount of fuel.  Do this in a properly ventilated area.

2.)  Remove the seat and rear fender assembly from the quad.

3.)  Remove and loosen the front fender assembly bolts and push/pull tabs as needed to remove the side panel assemblies as well.  Leaving the front fender assembly in place but loose and rotated forward, carefully unbolt and remove your stock fuel tank.

4.)  Drain the fuel from your stock tank in a well ventilated area.

5.)  Remove the stock petcock from the original tank.  You will have to drill out the hole in the new tank for your petcock to mount into.  Using a 9/16” drill, carefully drill out the petcock area hole trying to keep the hole on center as not to ruin the o-ring indentation area.  Shake out any loose particles from drilling and then install your petcock into the new tank using your original hardware.

6.)  Set the tank on the quad and working from the front to the rear of the tank, loosely bolt it into place.

7.)  The rubber o-rings and “J” shaped hooks can now be installed.  Study the pictures on the front of the page.  Using a standard end wrench, you can “fish” the o-ring up through the wiring and over the seat mount to ultimately attach back to the hook and frame.  This process is repeated for the other side.

8.)  Again, working from the front to the back, go ahead and tighten all of your mounting bolts and tighten the bolts that attach the tank to your front fenders.

9.)  The tabs that are located on the side shroud fender assembly should fit into the slots that are molded into the profile of your new tank.  If they are a tight fit, you may choose to cut one or more of the tabs off to relieve some pressure as they are not necessary.  Remember that you will not use the original side panels.

10.)  Install your stock seat mount onto the rear of the tank.

11.)  Now re-install your fuel lines.  You can now fill the tank with fuel and check for leaks.

12.)  Re-install the seat and rear fender assembly.  Go back and double check your work.

13.)  You are now ready for riding.  Enjoy your new Clarke tank !