Clarke Manufacturing Inc. 13388 S. Molalla Forest Rd. Molalla OR. 97038

Part # 1436 CRF450R FOUR STROKES 2002-2004

3.3 GALLON FUEL TANK

Thank you for purchasing a Clarke fuel tank.  The following instructions will help you install this tank on a CRF450R 2002-2004 four stroke motorcycle.  There may be some plastic shavings left in the tank from the manufacturing process.  You can use compressed air to blow out the tank.  You may also want to rinse out the tank using a small amount of fuel before installing it. **PLEASE NOTE: 2004 MODELS had very slight frame changes that will make this fuel tank fit with less frame clearance than on 2003-2003 models.  To remedy these issues, a piece of padding is provided to shim the rear of the tank slightly and provide stabilization to the entire fuel tank/frame setup.  The photos below show the padding properly affixed to the rear of the frame.  Zip Tie the pad as shown to replace the stock rubber unit that is supplied by the factory.  It is also recommended that you periodically remove the tank and clean any grit or debris from the areas of the tank that come in contact with the frame spars and cable assemblies. The instructions on the back side of this page will help you to quickly install your new tank.

O.E.M.

Clarke

Padding

PLEASE SEE THE REVERSE SIDE OF THIS PAGE FOR INSTALLATION INSTRUCTIONS

1.) Begin by removing your old tank, shrouds and petcock.  Drain your old tank in a well ventilated area.

2.) Install your original petcock outlet bracket in the new tank.

3.) Place the tank into the frame and push it into position.

4.) Align the front grommet on the new tank over the mounting hole and insert the factory bolt and aluminum sleeve into the grommet.  Then start the bolt in loosely.

5.) Transfer the rear seat mount stud and the rear strap mount screw to the new tank.

6.) Attach the rubber strap to the rear screw.

7.) Install all shroud bolts loosely on the tank section using the original 6mm shroud bolts.

After locating the shrouds to the correct position, tighten shroud bolts. Repeat this process

on the opposite side.

8.) Go back and tighten all bolts, hook up fuel line and fill with gas.

9.) Check for leaks.

10.) Re-install the seat and fasten the seat mount bolts securely.

11.) You are now ready for riding. Enjoy your new Clarke tank.