Clarke Manufacturing Inc. 13388 S. Molalla Forest Rd. Molalla OR. 97038

Part #11622 (2011-2012) KTM 350/250 SX-F

2.6 GALLON FUEL TANK

Thank you for purchasing a Clarke fuel tank.  The following instructions will help you install this tank on a 2011-2012 KTM 250/350 SX-F.  There may be some plastic shavings left in the tank from the manufacturing process.  You can use compressed air to blow out the tank.  You may also want to rinse out the tank using a small amount of fuel before installing it. The instructions on the back side of this page will help you to install your new tank.

PLEASE SEE THE REVERSE SIDE OF THIS PAGE FOR INSTALLATION INSTRUCTIONS

1.) Begin by draining your old tank in a well ventilated area. Now, remove the seat, shrouds and center mount bushing.

2.) At the back of the tank just below the seat area, there is a power cable connected to the pressure regulator. Disconnect this cable from the regulator.

3.)  Disconnect the fuel line at the quick connector below the left side of the tank by the throttle body.

You should now be able to remove the original tank from the frame.

4.) There are 4 screws holding the pressure regulator, unbolt them and pull the internal lines out until you can get to the couplings and the power plug.  The couplings have a gray release collar that must be pushed down into the female side to unlock the 4 clips that hold it in place.  This WILL be difficult and you may have to use a small flathead screwdriver to push the clips outward to get them to come free.  Once you have them disconnected you can unbolt the fuel pump and remove it.

5.) You can now install the pump and regulator into the new tank.  You can do this in pretty much the reverse order in which you took the unit apart. It may help to use a wire or similar item to fish and pull the

pump and regulator back through the tank.  Make sure to line up all rubber seals and that all the couplings are sealed and locked.

6.) You should now be able to mount the tank to the bike and reconnect the fuel line and cable to the regulator and re-install the center mount bushing and bolt.

7.) Now inspect your work and make sure the tank is tight and that it does not pinch or bind cables etc. that could inhibit the controls or function of the bike.

8.) Locate the shrouds to their correct position and then start the supplied 6mm shroud screws loosely to the tank. Using the factory radiator mount bolt, loosely install the lower shroud section to the radiator

mount.  Repeat on the opposite side and then tighten the screws down.

9.) Add some fuel to the tank and check for any leaks.

10.) The new tank includes a new seat mount button, make sure it is tight and then install your seat as usual.

11.) You are now ready for riding. Enjoy your new Clarke tank.