Clarke Manufacturing Inc. 13388 S. Molalla Forest Rd. Molalla OR. 97038

Part # 1318 1990-1999 DR350S and DR250S DUAL SPORT ONLY

4.2 GALLON FUEL TANK

Thank you for purchasing a Clarke fuel tank.  The following instructions will help you install this tank on a 1990-1999 DR350S or DR250S DUAL SPORT ONLY motorcycle.  There may be some plastic shavings left in the tank from the manufacturing process.  You can use compressed air to blow out the tank.  You may also want to rinse out the tank using a small amount of fuel before installing it. The instructions on the back side of this page will help you to install your new tank properly.

NOTE**:  1993-1995 models the vacuum chamber of the petcock touches the head and clearance should

be provided.  Follow the instructions on the back page and once the tank is loosely in position, you can then mark the area that is contacting and remove an amount of material from the top head fin.  It should

resemble the drawing in shape and depth.  Run the vacuum hose under the carburetor manifold.

SPECIAL NOTE FOR CALIFORNIA MODELS ONLY:  California dual sport models are equipped with

emissions controls ( i.e. charcoal canister etc..) This will need to be removed before mounting this tank.

Upon purchase and installation the consumer assumes liability and is solely responsible for compliance with all local and federal laws

PLEASE SEE THE REVERSE SIDE OF THIS PAGE FOR INSTALLATION INSTRUCTIONS

1.) Begin by removing your old tank, and petcock.  Drain your old tank in a well ventilated area.

2.)  This tank will use your original petcock however the spacer plate must be removed.  Install your original petcock in the new tank using the new petcock gasket in combination with the original

“oval o-ring” that is currently on your OE petcock.   ** NOTE:  On 1999 models, the choke lever

will interfere with the fuel line.  You will have to turn your petcock around so the line will clear

the choke area.  You may have to run a longer fuel line and possibly a longer vacuum line to accommodate this modification.

3.) Remove the rear bracket from the frame of your bike and connect it to the aluminum mounting plate that is supplied on the rear of the tank.

4.)  Loosen the carburetor at the air boot and head and rotate the top inward to provide clearance to

allow the petcock by the throttle cable.

6.) Remove the wire form “safety bar” from the Clarke tank and set it aside for later installation.

7.)  Now place the tank over the frame and push it forward into position on the rubber pucks that will slide into the plastic mounting brackets that are pre-installed on the tank.  Align the rear bracket assembly with their respective mounting holes at the back of the tank/frame.

8.)  Return the carburetor to a vertical position and re-connect the small tube to the side of the petcock

9.)  Secure the rear mount to the frame.

10.)  Fish the wire form “safety bar”  through the front part of the tank/frame area and fasten it to the tank

using the screws provided.

11.)  Fill the tank with fuel and check for leaks.

12.) Re-install the seat and fasten the seat mount bolts securely make sure all bolts are tight and the

petcock is secure.

13.) You are now ready for riding. Enjoy your new Clarke tank.

# Text boxes

1/8” Deep

1/2” Wide