Clarke Manufacturing Inc. 13388 S. Molalla Forest Rd. Molalla OR. 97038

Part # 1409 2000-2020 DRZ400SE and DRZ400SM

DUAL SPORT ONLY

3.9 GALLON FUEL TANK

Thank you for purchasing a Clarke fuel tank.  The following instructions will help you install this tank on a 2000-2020 DRZ400SE or DRZ400SM DUAL SPORT ONLY motorcycle.  There may be some plastic shavings left in the tank from the manufacturing process.  You can use compressed air to blow out the tank.  You may also want to rinse out the tank using a small amount of fuel before installing it. The instructions on the back side of this page will help you to install your new tank properly.  SPECIAL NOTE FOR CALIFORNIA MODELS ONLY:  California dual sport models are equipped with

emission controls ( i.e. charcoal canister etc..) This will need to be removed before mounting this tank.

Upon purchase and installation the consumer assumes all liability and is solely responsible for compliance with all local and federal laws

PLEASE SEE THE REVERSE SIDE OF THIS PAGE FOR INSTALLATION INSTRUCTIONS

1.) Begin by removing your old tank, and petcock.  Drain your old tank in a well ventilated area.

Also, separate the spacer from it (You will not need it)

2.) Install your original petcock in the new tank using the new petcock gasket in combination with the original “oval o-ring” and the fiber washers that are currently on your OE petcock.

3.) Remove the wire form “safety bar” from the Clarke tank and set it aside for later installation.

4.) Now place the tank over the frame and push it forward into position on the rubber pucks that will slide into the plastic mounting brackets that are pre-installed on the tank

5.) Align the rear of the tank with their respective mounting holes at the back of the tank/frame.

Using your factory grommet spacer/inserts and the factory bolts, affix the tank to the rear mounts.

You may be required to loosen the grommets and align then tighten now you are complete.

6.) Now install your seat, carefully aligning the groove on the seat base with the new rear spine mount that is included on the tank.

7.) Fish the wire form “safety bar” through the front part of the tank/frame area and fasten it to the tank

using the screws provided.

8.)  Now install your shrouds using the new screws that are provided with the tank.

9.) Go back and make sure all bolts are tight and hook up your fuel line.  You may need to run a longer

fuel line as well as a longer vacuum tube line as they may become kinked due to the larger size of the

new tank.  A kinked line may result in poor starting, idling or running.

10.)  Fill the tank with fuel and check for leaks.

11.) You are now ready for riding. Enjoy your new Clarke tank