Clarke Manufacturing Inc. 13388 S. Molalla Forest Rd. Molalla OR. 97038

Part # 1460 2004-2005 KX-F 250 and 2004-2006 RM-Z 250

2.3 GALLON CAPACITY FUEL TANK

Thank you for purchasing a Clarke fuel tank.  The following instructions will help you install this tank on a 2004-2005 KX-F250 or 2004-2006 RM-Z250 motorcycle.  There may be some plastic shavings left in the tank from the manufacturing process.  You can use compressed air to blow out the tank.  You may also want to rinse out the tank using a small amount of fuel before installing it. The instructions on the back side of this page will help you to quickly install your new tank

PLEASE SEE THE REVERSE SIDE OF THIS PAGE FOR INSTALLATION INSTRUCTIONS

1.) Shut off fuel supply and disconnect fuel line and remove your old tank, shrouds and petcock.  Drain your old tank in a well ventilated area.

2.) Install your original petcock in the new tank.

3.) Remove the bolts, washers and the aluminum bracket from the Clarke tank.

4.) Using the tapered head allen screw supplied with the bracket, bolt the bracket to the frame in the stock

front mount location.

5.) Now fit the tank into the frame cradle and align the front mount bracket with the rubber grommets and spacers.

6.) Using the supplied 6mm x 35mm bolts, attach and tighten the tank to the bracket.

7.) Align the front mount brackets with the area they bolt to and using the factory bolts, affix the tank to frame.

8.) Transfer the rear seat mount stud and the rear strap mount screw to the new tank.

9.) Attach the rubber strap to the seat screw.

10.) Go back and tighten all bolts, hook up the fuel line and fill with gas.

11.) Check for leaks.

12.) Re-install the radiator shrouds and seat.

13.) You are now ready for riding. Enjoy your new Clarke tank.