Clarke Manufacturing Inc. 13388 S. Molalla Forest Rd. Molalla OR. 97038

Part # 1463 HUSQVARNA FOURSTROKES 2005-2006

3.7 GALLON FUEL TANK

Thank you for purchasing a Clarke fuel tank.  The following instructions will help you install this tank on a Husqvarna 2005-2006 four stoke motorcycle.  Please install this tank only in a well ventilated area.

There may be some plastic shavings left in the tank from the manufacturing process.  You can use compressed air to blow out the tank.  You may also want to rinse out the tank using a small amount of

fuel before installing it.  We recommend that this tank be installed by a qualified mechanic.  If you have

any questions, please call first before installing.

1.) Begin by removing your old tank, shrouds and petcock.  Drain your old tank in a well ventilated area.

2.) Install your original petcock in the new tank.

3.) Fit the new tank to the bike but do not bolt it tight yet.

4.) To achieve the additional fuel capacity, this tank has been modified from the original shape and size.

Due to these changes, your OEM radiator shrouds will not properly fit without first being trimmed.

The pictures and instructions on the back of this page will help you to achieve a good result and a nice looking match where the tank and shrouds meet.

Look at the pictures at the top of the back of this page and note that the factory tank covers ( blue ) are not used, they will NOT have to be cut.  The lower front grey shrouds are the plastic pieces that need to be trimmed to fit.  This process will be repeated for both the left and right side shrouds.

It is recommended that you use a very sharp razor knife, shears or similar to cut the plastic.

The general idea will be to fit the shrouds to their positions with the now loosely installed tank, then

mark the area on the shrouds that need to be trimmed and carefully trim the areas necessary for a good

fit.  Remember to go slowly, and that it is better to cut off less than you need to and then trim to fine tune the fit to your liking.

BEFORE                                                                          AFTER

TRIMMING INSTRUCTIONS

Picture 1.)  Mark a line 9/16” down from the top of the rear flange.  Use some masking tape to give you a

better line to follow when cutting. Trim away this section.

Picture 2.)  Now mark 3/4” from the top of the front flange and trim this away as well.

Picture 3.) On the backside of the shroud you will find the molded in air deflector.  Mark the piece as shown

in the picture and cut carefully.  Make sure not to cut away the outside face of the shroud.

Picture 4 .) Measure 1- 7/8” from the rear top edge forward and mark it.  Measure 1- 3/4” from the bottom

rear edge forward along the edge and make another mark.  Draw a line between the 2 marks and trim away

the shroud corner.

PICTURE 1.                          PICTURE 2.                       PICTURE 3.                        PICTURE 4.

Now fit the shrouds to their locations to determine whether or not additional trimming is required.

Continue to fit and trim until the look is to your satisfaction.  Once the shrouds are in place for final fitting,

bolt the tank down tight and reinstall the seat and fasten the rear panels to the back part of the tank.  Hook up

your fuel line and fill the tank with fuel.  Check for leaks. You are now ready to enjoy your new Clarke tank.