Clarke Manufacturing Inc. 13388 S. Molalla Forest Rd. Molalla OR. 97038

Part # 1466 RMZ 450 FOUR STROKE 2005-2006

3.1 GALLON FUEL TANK

Thank you for purchasing a Clarke fuel tank.  The following instructions will help you install this tank on a RMZ 450 2005-2006 four stroke motorcycle.  There may be some plastic shavings left in the tank from the manufacturing process.  You can use compressed air to blow out the tank.  You may also want to rinse out the tank using a small amount of fuel before installing it. This tank will not use your original front tank mount but instead utilizes a pair of “L” shaped brackets to hold the tank in the frame and prevent it from lifting. The instructions on the back side of this page will help you to quickly install your new tank

PLEASE SEE THE REVERSE SIDE OF THIS PAGE FOR INSTALLATION INSTRUCTIONS

1.) Begin by removing your old tank, shrouds and petcock.  Drain your old tank in a well ventilated area.

2.) Install your original petcock in the new tank.

3.) Remove the “L” shaped brackets from the Clarke fuel tank.

4.) Place the tank into the frame and push it into position.

5.) Re-install the “L” brackets to the tank and tighten the bolts to assure that the fuel tank is secure.

6.) Transfer the rear seat mount stud and the rear strap mount screw to the new tank.

7.) Attach the rubber strap to the rear screw.

8.) Install all shroud bolts loosely on the tank section using the original shroud bolts.

After locating the shrouds to the correct position, tighten shroud bolts. Repeat this process

on the opposite side.

9.) Go back and tighten all bolts, hook up fuel line and fill with gas.

10.) Check for leaks.

11.) Re-install the seat and fasten the seat mount bolts securely.

12.) You are now ready for riding. Enjoy your new Clarke tank.