Clarke Manufacturing Inc. 13388 S. Molalla Forest Rd. Molalla OR. 97038

Part # 1482 KAWASAKI KX450F (2006-2008)

3.1 Gallon Fuel Tank

Thank you for purchasing a Clarke fuel tank.  The following instructions will help you install this tank on a KX450F 2006-2008 four stroke motorcycle.  There may be some plastic shavings left in the tank from the manufacturing process.  You can use compressed air to blow out the tank.  You may also want to rinse out the tank using a small amount of fuel before installing it. This tank will fit without any modification on the bike itself, but will require the use of the included front mount bracket. The instructions on the back side of this page will help you to quickly install your new tank

PLEASE SEE THE REVERSE SIDE OF THIS PAGE FOR INSTALLATION INSTRUCTIONS

1.) Begin by removing your old tank, shrouds and remote petcock outlet assembly.  Drain your old tank in            a well ventilated area.

2.) Install your original remote petcock assembly onto the new tank using your original hardware.

3.) Take the supplied front mount bracket assembly and unbolt it from the tank.  Insert your factory front mount bolt and washer down through the center of the bracket and bolt it firmly to the original mounting area on the bike.

4)  Place the tank into the frame and push it into position aligning the tank over the bracket so the inserts on the bottom of the tank line up with the holes on the outer ends of the bracket.

5.) Using the supplied screws and washers, bolt the bracket to the underside of the tank.

It is recommended that you use “Blue Lock-Tite” to ensure that the bolts stay in.

6.) Transfer the forward seat mount stud and the rear strap mount screw to the new tank.

7.) Install all shroud bolts loosely on the tank section using the original shroud bolts.

After locating the shrouds to the correct position, tighten shroud bolts. Repeat this process on the

opposite side.

8.) Attach the rubber strap to the rear screw, hook up fuel line and fill with gas.

9.) Check for leaks.

10.) Re-install the seat and fasten the seat mount bolts securely.

11.) You are now ready for riding. Enjoy your new Clarke tank.