1-800-232-2002 / www.clarkemfg.com

Clarke Manufacturing Inc. 13388 S. Molalla Forest Rd. Molalla OR. 97038

Part #11611 YAMAHA TW200 FUEL TANK

2.7 GALLON FUEL TANK

Thank you for purchasing a Clarke fuel tank.

The following instructions will help you install this tank

PLEASE SEE THE REVERSE SIDE OF THIS PAGE FOR INSTALLATION INSTRUCTIONS

Step 1.  After unpackaging your Clarke tank and reading the instructions be sure to thoroughly blow out your tank with compressed air followed by a rinse with fuel. Be sure to wear eye protection and rubber gloves to protect yourself from the plastic chips that may be still in the tank and from the fuel used to rinse out the fine particles remaining. We also recommend doing this outdoors as fumes from the fuel are dangerous and could ignite and are a health hazard. A respirator is also a good idea and highly recommended!

Step 2. Following the service manual for your bike, remove the fuel tank and the rear lower grommet plate from the bike, you will reuse the top grommet plate in step 4. Once the tank is off the bike be sure to drain the remaining fuel out of the tank. After the fuel has been drained from the tank you may unbolt the old petcock and install it onto the new tank, check for leaks by adding a small amount of fuel. If no leaks are found proceed to step 3, if it does leak try replacing the original O-ring on the petcock with the supplied petcock gasket. We do not recommend stacking both O-ring and gasket to get the petcock to seal. You will also leave the original round front rubber tank mounts in place as this helps keep the tank centered.

Step 3. Place the top grommet mount that was removed in step 2 back onto the bike. It will need to be placed upside down with the angle facing up and towards the rear of the bike. Now you may place the tank on to the bike for a test fit. If all looks well install the front mounting bolt into place but do not tighten the nut down, finger tight is fine. Reinstall the original rear bolt and washer, do not tighten at this time.

Step 4. Reinstall your side panels and adjust your tanks location until proper side panel fit is achieved, the side panels should just plug into the rear tank grommets. You may or may not have to raise or lower the rear of the tank. To raise you will have to add washers which are not supplied. To lower you may remove the grommet plate but you may need a washer or two under the bolt to supply correct clamping force to the rear grommet. After a good fit is achieved you may tighten down the tank bolts. The proper way to tighten the front bolt is to tighten the lock nut down until it just contacts the flat washer then tighten an additional half turn.

Step 5.Locate the vent line that connected to the bottom of the original tank. This hose is the vent line for the carburetor and will need to be redirected downwards to behind the engine/ swing arm area. Make sure it hangs down a few inches below the bike and if necessary trim to length. If you have a bike sold in California you will only need to plug that vent line. Parts for this are not included.

Step 6. Add a small amount of fuel and double check for leaks, if leaks are found correct them before riding. If no leaks are found you may fill the tank. You are now ready to ride, enjoy your new Clarke tank!