Clarke Manufacturing Inc. 13388 S. Molalla Forest Rd. Molalla OR. 97038

Part # 1469 2006-2007 YZ-F450 and YZ-F250

2.6 GALLON FUEL TANK

Thank you for purchasing a Clarke fuel tank.  The following instructions will help you install this tank on a 2006-2007 YZ-F450 or YZ-F250 motorcycle.  There may be some plastic shavings left in the tank from the manufacturing process.  You can use compressed air to blow out the tank.  You may also want to rinse out the tank using a small amount of fuel before installing it. The instructions on the back side of this page will help you to install your new tank properly.

PLEASE SEE THE REVERSE SIDE OF THIS PAGE FOR INSTALLATION INSTRUCTIONS

1.) Begin by removing your old tank, large upper frame pad, shrouds and petcock.

Drain your old tank in a well ventilated area.

2.) Install your original petcock in the new tank.

3.) Included with the tank are 2 pieces of rubber padding and 2 zip-ties ( 11” ).

Using the zip-ties, attach each piece of padding to the frame spars as shown in Photo 3 on the front page.  Make sure to locate them on the sides of the frame spars as depicted.  This step will help to protect your frame and also spreads the tank out to provide better clearance.

4.)  Now place the tank into the frame and push it into position.

5.) Transfer the rear seat mount stud to the new tank.

6.) Align the front mount area over the factory hole in the frame. Push the tank firmly forward and loosely

affix the tank to the mount using your original bolt.  Install the rear of the tank using the original bolt as well.

7.) Install all shroud bolts loosely on the tank section using the original shroud bolts and loosely install

the radiator mount bolts.

8.) Now go back and tighten the frame mounting bolts as well as the shroud and radiator mount bolts.

9.) A section of fuel line is provided with this tank.  Attach the line to the petcock and route it to the carburetor

as shown in Picture 1 on the front page.  Turn the petcock to the OFF position and fill the tank with fuel.

10.) Check for leaks.

11.) Re-install the seat and fasten the seat mount bolts securely.

12.) You are now ready for riding. Enjoy your new Clarke tank.

# Text boxes

Picture 1

Picture 2

Picture 3