Clarke Manufacturing Inc. 13388 S. Molalla Forest Rd. Molalla OR. 97038

PART #SFLA 1979-1981 TT/XT500

3.5 Gallon Universal Tank

Thank you for purchasing a universal Clarke fuel tank.  Universal fuel tanks are provided to fill the need for an application that has no specific tank available for direct installation.  Universal tanks are NOT application specific and are not intended to fill a need for every bike ever made.

The part #SFLA has been sold for many years as an excellent plastic replacement tank for the XT/TT500 motorcycle.  This sheet is intended as mounting instruction for these bikes.  This tank is “universal”, however, we have provided special hardware to install as closely to the original equipment as possible.  Generally speaking, universal tanks will ONLY fit Pre-1983, air cooled and dual-shocked motorcycles.  ALL universal tanks will require light to moderate modification for proper fitment.  Using a bit of common sense, a little ingenuity and some patience will allow you to successfully complete your project.  The following page is intended as suggested instructions and tips to mount your new tank. There may be some plastic shavings left in the tank from the manufacturing process.  You can use compressed air to blow out the tank.  You may also want to rinse out the tank using a small amount of fuel before installing it.

Locate and Drill ¼” Hole Here                               Carriage Bolt Will Be Pre-Installed

For Mounting Bolt:                                                  Here:

Drawing is Mounting Bracket (2)

PLEASE SEE THE REVERSE SIDE OF THIS PAGE FOR INSTALLATION INSTRUCTIONS

1.) Begin by removing your old tank, seat and petcock.  Drain your old tank in a well ventilated area.

2.) Place the tank down on the frame, put your seat on and position the tank so the rear of the tank touches the seat and raise the tank up to the desired position.  If the frame still has original frame pads and the tank looks to be OK on them go ahead and use the original padding.  If you need to shim the tank up or replace the old padding use the new padding that is provided with the tank.  You can secure the padding using zip ties or duct tape.

3.)  Once the tank is in the desired position and the seat is in place, your new front mount bracket holes can be located and drilled.  With the front aluminum brackets installed on the tank, rotate the bracket until it aligns over the stock mounting hole.   Do this on both sides, marking the location of the mount and then remove the tank.  The marks on the brackets are where you will be drilling the holes for the new bolt to go through and fasten to your factory mount.  Use a center punch for accuracy, and then use a 1/8” drill to drill a pilot hole drilling one side and then the other.  You can then use a ¼” or slightly larger drill to finish the hole on each side.  Do not bolt the tank to the bike until you install the petcock as described in the next step.

4.)  Determine which side of the tank the petcock needs to be mounted to.  Locate the center of the area where the petcock bolts to and mark it. You will be able to use your factory petcock or the Clarke petcock that is supplied with the tank.  Again, use a center punch to mark the hole location(s)  to keep the drill from wandering.  Using a ¼” bit, drill the hole(s) for the fuel to come out of. Once the hole(s) are drilled you can install the petcock using the o-ring or gasket and screws provided.

5.) You can now do the final install of the tank.  Put the tank back down on the frame and align the front mount brackets over the frame mounting locations. Using the lock washers and bolts provided, fasten the

brackets to the factory mount and tighten down.

6.)  At the rear of the tank there is an o-ring and a clip.  Make sure the clip bolt is tight.  Most steel tanks mount using a bolt or stud that is at the rear of the frame.  Take the bolt or stud and fasten it to its original position.  Take the o-ring and put it around the stud, twist it once, and hook it to the clip.  If it is too long make a double loop to shorten it. If there is no bolt or frame section to hook the o-ring on you will have to use a wire wrapped around the frame and through the o-ring.

7.) Turn the petcock to the OFF position and hook up your fuel line from the carburetor.  Fill the tank with fuel and check for leaks.

8.) Re-install the seat and fasten the seat mount bolts securely.  Go back and make sure all bolts are tight.

9.) You are now ready for riding. Enjoy your new Clarke tank.