Clarke Manufacturing Inc. 13388 S. Molalla Forest Rd. Molalla OR. 97038

Part # 1420 YAMAHA BANSHEE

5.5 GALLON CAPACITY FUEL TANK

Thank you for purchasing a Clarke fuel tank.  This tank is intended for use on a Yamaha Banshee. There may be some plastic shavings left in the tank from the manufacturing process.  You can use compressed air to blow out the tank.  You may also want to rinse out the tank using a small amount of fuel before installing it.  **PLEASE NOTE: For this tank to be properly installed it will require that the front fender assembly be altered to accommodate the size of the tank. Trimming of the fender is irreversible. It is recommended that if you are having difficulty understanding the following procedure that you call for assistance before attempting to install the tank.  By purchasing this tank you are accepting sole responsibility for any damage or problems that may arise from improper installation or failure to follow the instructions below.

PLEASE SEE THE REVERSE SIDE OF THIS PAGE FOR INSTALLATION INSTRUCTIONS

1.) Begin by removing the original rear fender and seat as well as the front fender assembly and

original vented side panels.

2.) Shut off fuel supply and disconnect the fuel line and remove the original tank and petcock.

drain your old tank in a well ventilated area.

3.) Install your original petcock to the new tank using the supplied petcock flat gasket and your

OEM o-ring gasket.

4.) Carefully examine the drawing on the front of this page.  You will need to cut the side panels

as shown to provide clearance for the new tank.  This cut should be made carefully using a

hacksaw or very sharp utility knife.

5.) Cut should be made as shown in Figure 1 approximately 12 inches from the rear tab mount making sure to follow the natural angle of the fender.  This step will need to be repeated for both sides.

6.) Now remove the original metal bushings from the rear mounts of the old tank and install them by sliding them into the new rubber grommets at the rear of the new tank.

7.) Using the original rear mounting bolts, mount the rear of the tank loosely.

8.) Mount the front of the tank using the slotted brackets provided.  Use the 6mm bolts in the slotted portion of the mount and bolt to the brass tank inserts.  Adjust the tank to align the 5mm bolts over their mounting points.  Once you have all bolts started loosely and the tank is where you like it, go back and

tighten all the mounting bolts.

9.) Install the gas line and make sure the hoses are routed properly to the carburetors.

10.) Make sure your petcock is turned to “off” and fill the tank with fuel.  Check for any leaks.

11.)  You can now re-install the front fender assembly (minus the now cut side panels and vented side panels ) and front radiator shroud louver.

12.) Re-install the seat and rear fender assembly.  Enjoy your new Clarke tank.