Clarke Manufacturing Inc. 13388 S. Molalla Forest Rd. Molalla OR. 97038

Part # 1392 ATC250SX  ALL YEARS

STOCK CAPACITY FUEL TANK

Thank you for purchasing a Clarke fuel tank.  This tank is intended use on the ATC250SX. There may be some plastic shavings left in the tank from the manufacturing process.  You can use compressed air to blow out the tank.  You may also want to rinse out the tank using a small amount of fuel before installing it.  Please note: When installing this tank on a 1985 model ATC250SX, you may have to use a bit more force to get the tank to go down onto the frame.  The plastic is extremely durable and you will not damage it as long as no sharp tools are used.

PLEASE SEE THE REVERSE SIDE OF THIS PAGE FOR INSTALLATION INSTRUCTIONS

1.) Shut off fuel supply and disconnect fuel line and remove the original tank and petcock.  Drain your old tank in a well ventilated area.

2.) Remove the safety bar from inside the tank and set it aside for final installation.

3.) Install your original petcock to the new tank carefully threading it onto the supplied aluminum petcock adapter.

4.) Slide the tank onto the front rubber mounting pucks.

5.) Use your original rear mount bolt to bolt the new tank tightly to the rear mount hole.

6.) Take the safety bar and slide it across and under the front part of the frame and using the supplied

phillips head screws, affix the safety bar to the tank on both sides.  The safety bar is simply an extra precaution to keep the tank from lifting off of the frame.

7.) Now hook up the fuel line, turn the petcock to the OFF position and fill the tank with gas.

8.) Check for leaks.

9.) Re-install the rear fender and seat assembly.

10.) You are now ready for riding. Enjoy your new Clarke tank.