Clarke Manufacturing Inc. 13388 S. Molalla Forest Rd. Molalla OR. 97038

Part # 1396 ATC70 ALL YEARS

STOCK CAPACITY FUEL TANK

Thank you for purchasing a Clarke fuel tank.  This tank is intended use on the ATC70. There may be some plastic shavings left in the tank from the manufacturing process.  You can use compressed air to blow out the tank.  You may also want to rinse out the tank using a small amount of fuel before installing it.

PLEASE SEE THE REVERSE SIDE OF THIS PAGE FOR INSTALLATION INSTRUCTIONS

1.) Shut off fuel supply and disconnect fuel lines and remove the original tank and petcock hoses.  Drain your old tank in a well ventilated area.

2.) Slide the tank onto the front rubber mounting pucks aligning the rear mount hole/grommet over the mounting hole on the frame.

3.) Using your factory bolt, affix the tank to the rear mount and tighten it down.

4.) Now hook up the fuel lines, turn the petcock to the OFF position and fill the tank with gas.

5.) Check for leaks.

6.) Re-install the rear fender and seat assembly adjusting fit as necessary with the tank.

7.) You are now ready for riding. Enjoy your new Clarke tank.