Clarke Manufacturing Inc. 13388 S. Molalla Forest Rd. Molalla OR. 97038

Part # 1461 GAS GAS FSE 450 FOUR STROKE 2005-2006

2.8 GALLON FUEL TANK

Thank you for purchasing a Clarke fuel tank.  The following instructions will help you install this tank on a Gas Gas 450 FSE 2005-2006 model four stroke motorcycle.  There may be some plastic shavings left in the tank from the manufacturing process.  You can use compressed air to blow out the tank.  You may also want to rinse out the tank using a small amount of fuel before installing it. This tank will require the use of the included front mount bracket. The instructions on the back side of this page will help you to quickly install your new tank

PLEASE SEE THE REVERSE SIDE OF THIS PAGE FOR INSTALLATION INSTRUCTIONS

1.) Begin by removing your old tank, shrouds, seat and fuel injection unit.  Drain your old tank in a well ventilated area.  Make sure to be careful unhooking the fuel injection computer and fuel injection unit.

2.) Remove the computer box from the bottom of the original tank and transfer it to the new Clarke tank using the supplied 1.00 spacers and 5mm x 40mm pan head screws.

3.) Remove the fuel pump assembly from your original tank.  Using the stock bolts, mount the injection unit to the new Clarke tank making sure the seal is not bound and fits tight.  Go ahead and tighten down all the bolts for the unit.

4)  Now put a small amount of fuel into the tank and tip it forward so the gas is located over the fuel pump area.  Check for any leakage around the pump seal.

5.) Transfer the rear seat mount stud to the new tank using the supplied 5mm screw.  The tank is now ready for installation.

6.) Align the tank into the frame and plug in the computer box and fuel pump connectors from the

wiring harness.

7.) Attach the fuel line from the pump to it’s original hook up.

8.) The new tank is supplied with a new custom front mount bracket that has been loosely pre-installed

to the tank at our factory.  You will need to remove your stock hose barb that your OEM vent hose is

attached to.  This location is where the new front mount bracket will bolt to.  The picture on the front

of the page depicts the orientation of the bracket.  Make sure the bracket is bolted tightly to the tank

and then align the bracket over the hole and affix it to the frame using the supplied 6mm x 16mm

pan head screw.

9.) Re-Attach the rubber tank strap to it’s original location.

10.) Install the radiator shrouds using the 6mm pan head screws that are supplied with the new tank.

11.) Now fill the tank with fuel and check for any leaks.

12.)  Re-install the seat and fasten the seat mount bolts securely.

13.)  Go back and make sure all bolts and screws are secure.  You are now ready for riding.

Enjoy your new Clarke tank.