Clarke Manufacturing Inc. 13388 S. Molalla Forest Rd. Molalla OR. 97038

Part # 1464 ATC250R 1985-1986 MODELS

STOCK CAPACITY FUEL TANK

Thank you for purchasing a Clarke fuel tank.  The following instructions will help you install this tank on an ATC250R 1985-1986 model three wheeler.  There may be some plastic shavings left in the tank from the manufacturing process.  You can use compressed air to blow out the tank.  You may also want to rinse out the tank using a small amount of fuel before installing it. The instructions on the back side of this page will help you to quickly install your new tank

PLEASE SEE THE REVERSE SIDE OF THIS PAGE FOR INSTALLATION INSTRUCTIONS

1.) Begin by removing your old tank, shrouds and petcock.  Drain your old tank in a well ventilated area.

2.) Install your original petcock in the new tank.

3.) Remove the aluminum bushings from the original rubber grommets located in your original front mounts and take the rubber grommets out.

4.) Install the rubber grommets into the front mount brackets of the new tank and install the aluminum spacers into them like the original unit.

5.) Place the tank into the frame and push it into position.

6.) Now align the molded in rear brackets with the rear mount section of the ATC and using your factory bolts and the washers provided, bolt the tank down in the rear.

7.) Align the front mount brackets with the area they bolt to and using the factory bolts, affix the tank to frame.

8.) Now go back and make sure all bolts are tight.

9.) Re-install the radiator shrouds and hook up the fuel line and fill with gas.

10.) Check for leaks.

11.) Re-install the rear fender assembly and seat.

12.) You are now ready for riding. Enjoy your new Clarke tank.