Clarke Manufacturing Inc. 13388 S. Molalla Forest Rd. Molalla OR. 97038

Part #11618 CRF230F AND CRF150F 2008-2009 AND 2012

2.9 GALLON FUEL TANK

Thank you for purchasing a Clarke fuel tank.  The following instructions will help you install this tank on a 2008-2009 AND 2012 CRF230F and CRF150F motorcycle.  There may be some plastic shavings left in the tank from the manufacturing process.  You can use compressed air to blow out the tank.  You may also want to rinse out the tank using a small amount of fuel before installing it. The instructions on the back side of this page will help you to install your new tank properly.

PLEASE SEE THE REVERSE SIDE OF THIS PAGE FOR INSTALLATION INSTRUCTIONS

1.) Begin by removing your old tank, seat, shrouds and petcock.  Drain your old tank in a well ventilated area.

2.) Install your original petcock in the new tank using your original o-ring and bolts

3.) Transfer the original set of front mounts from your original tank to the new tank using the hardware that is supplied by the original manufacturer.

4.) Note the 4 “L” brackets that are installed at the four corners of the tank.  These are for your shrouds to mount to.  Position these close to their proper location and then proceed to fit the tank on the frame.

5.) Now place the tank over the frame and push it into position. Align the bushing area with the mounting holes on the frame and get one bolt partially started, then move to the other side and start the other bolt in.  Once both mounting bolts are started go back and tighten them down.

6.)  Now align the “L” brackets to their proper location using the shrouds as a guide and then tighten them firmly to the tank.  Now, using your stock shroud screws, affix the shrouds to the tank wall.  Then, using the stock shroud fasteners, push them through the shroud mount holes and the “L” brackets slot for a firm fit.

7.) This tank includes a new hex head bolt for your seat mount assembly to fasten to.  Using your original seat mount strap assembly, fasten it to the hex head bolt.

8.) Now go back and make sure everything is tight and in place.

9.) Turn the petcock to the OFF position and fill the tank with fuel.  Check for leaks.

10.) Re-install the seat and fasten the seat mount bolts securely

11.) You are now ready for riding. Enjoy your new Clarke tank.