Clarke Manufacturing Inc. 13388 S. Molalla Forest Rd. Molalla OR. 97038

Part # 1305 CR125 (89-90) and CR500R (89-00) and (1991+)

Part #1302 CR250R (88-89)

3.5 GALLON FUEL TANK

Thank you for purchasing a Clarke fuel tank.  The following instructions will help you install this tank on the above CR motorcycles.  There may be some plastic shavings left in the tank from the manufacturing process.  You can use compressed air to blow out the tank.  You may also want to rinse out the tank using a small amount of fuel before installing it. The instructions on the back side of this page will help you to install your new tank properly.

PLEASE SEE THE REVERSE SIDE OF THIS PAGE FOR INSTALLATION INSTRUCTIONS

1.) Begin by removing your old tank, shrouds and petcock.  Drain your old tank in a well ventilated area.

2.) Install your original petcock in the new tank using the original hardware and o-ring/

3.) Loosen and reverse the top hose clamps.  The screw adjuster should be toward the radiator

4.) Slide the hoses down ¼” to the straight part of the inlet.  The clamps to the balance tube should also be loosened and rotated down.

5.) The new tank will not use the original mounts.  Using the steel sleeve portion of your mount, install the sleeve in the grommet mount small end out.  Put the spacer supplied down the hole and over the small end of the steel sleeve.

6.) Now, using your original factory bolt secure the tank to the frame.

7.) The tank may be a tight fit going over the mounts.  You can spread the tank by putting some air in thru the cap vent.

8.) Transfer the rear seat mount bracket and the rear strap mount screw from your original tank

to the new tank.

9.) Install all shroud bolts loosely on the tank section using the original shroud bolts and loosely install

the radiator mount bolts.

10.) Now tighten the shroud and radiator mount bolts and attach the rubber strap to the rear screw.

11.) Turn the petcock to the OFF position and fill the tank with fuel.

12.) Check for leaks.

13.) Re-install the seat and fasten the seat mount bolts securely.

14.) You are now ready for riding. Enjoy your new Clarke tank.