Clarke Manufacturing Inc. 13388 S. Molalla Forest Rd. Molalla OR. 97038

Part # 1316 XR250L

4.0 GALLON FUEL TANK

Thank you for purchasing a Clarke fuel tank.  The following instructions will help you install this tank on the X250L motorcycle.  There may be some plastic shavings left in the tank from the manufacturing process.  You can use compressed air to blow out the tank.  You may also want to rinse out the tank using a small amount of fuel before installing it. The instructions on the back side of this page will help you to install your new tank properly.  If you have any questions, please call us before you install the tank.

PLEASE SEE THE REVERSE SIDE OF THIS PAGE FOR INSTALLATION INSTRUCTIONS

1.) Begin by removing your old tank and petcock.  Drain your old tank in a well ventilated area.

2.)  Install the petcock from your old tank onto the new one by inserting it into the tank and carefully

threading it onto supplied petcock adapter but do not tighten it all the way down yet.

3.) Cut the padding provided into 4 pieces. The padding is supplied to provide more stability to the tank since there are no support pads as is typical on most plastic tank applications.

4.) Zip-Tie or duct tape them to the front and rear section of the frame as shown in the diagram.

5.) Remove the front bolt and 2 spacers.  Now place the tank over the frame and push it forward.

There is an existing hole in the gusset plate that you want to align the front tank grommets over.

6.) Start the bolt through the tank and install 1 small spacer on each side of the frame.  Add the washer and nut and tighten the bolt.

7.) The rear of the tank is held with a large O-ring.  Loop it around the 2 ears of the existing lower rear mount, pulling the section of the O-ring closest to the tank up and hook it over the screw that is protruding from the rear of the tank.

8.) Now hook up the gas line to get the proper fit and direction of the petcock and tighten the petcock nut fully.

9.) Fill up the tank and check for leaks.

10.) Now re-install the seat and check to make sure that all the bolts are tight.

11.) You are now ready to enjoy your new Clarke tank.  Happy riding!

# Text boxes

PADS

FRAME