Clarke Manufacturing Inc. 13388 S. Molalla Forest Rd. Molalla OR. 97038

Part # 1323 TRX70

STOCK CAPACITY FUEL TANK

Thank you for purchasing a Clarke fuel tank.  This tank is intended for use on the TRX70. There may be some plastic shavings left in the tank from the manufacturing process.  You can use compressed air to blow out the tank.  You may also want to rinse out the tank using a small amount of fuel before installing it. Please note that the stock hole on the tank cover/front fender assembly must be enlarged approximately 1/8” to accommodate the new gas cap.  Mark the area to be trimmed away around the circumference of the hole and remove material using a very sharp razor knife.  Avoid large cuts and go slow for best results.

PLEASE SEE THE REVERSE SIDE OF THIS PAGE FOR INSTALLATION INSTRUCTIONS

1.) Remove the rear seat and fender assembly.  Also remove the front fender assembly.

2.) Shut off fuel supply and disconnect fuel lines and remove the original tank and petcock hoses.

Drain your old tank in a well ventilated area.

3.) Slide the tank onto the front rubber mounting pucks and align the tank with the original rear frame mount.  Using the bolt and washer provided, bolt the rear of the tank tightly to the frame.

4.) Now hook up the fuel lines, turn the petcock to the OFF position and fill the tank with gas.

5.) Check for leaks

6.) Re-install the front fender assembly and rear fender and seat assembly taking care to make sure

all bolts are re-installed and tight.

7.) You are now ready for riding. Enjoy your new Clarke tank.