Clarke Manufacturing Inc. 13388 S. Molalla Forest Rd. Molalla OR. 97038

Part # 1324 1988-1992 TRX300 and Part #1325 1993-2002 TRX300

STOCK CAPACITY FUEL TANK

Thank you for purchasing a Clarke fuel tank.  These tanks are intended for use on a TRX300.  Please note that these tanks are for the 2 Wheel Drive models only. They will fit 4 x 4 models but there will be a large gap between the tank and seat junction.  There may be some plastic shavings left in the tank from the manufacturing process.  You can use compressed air to blow out the tank.  You may also want to rinse out the tank using a small amount of fuel before installing it.

PLEASE SEE THE REVERSE SIDE OF THIS PAGE FOR INSTALLATION INSTRUCTIONS

1.) Shut off fuel supply and disconnect fuel line and remove the original tank and petcock.  Drain your old tank in a well ventilated area.

2.) Install your original petcock to the new tank carefully threading it onto the supplied aluminum petcock adapter.

3.) Slide the tank onto the front rubber mounting pucks.

4.) Use your original rear mount bolt to bolt the new tank tightly to the rear mount hole.

5.) Now hook up the fuel line, turn the petcock to the OFF position and fill the tank with gas.

6.) Check for leaks.

7.) Re-install the rear fender and seat assembly. Make sure to “plug in” the side panels to the rear tabs of the tank.

8.) You are now ready for riding. Enjoy your new Clarke tank.