Clarke Manufacturing Inc. 13388 S. Molalla Forest Rd. Molalla OR. 97038

Part # 1387 XR650L ALL YEARS or XR600R 1988-2000

4.0 GALLON FUEL TANK

Thank you for purchasing a Clarke fuel tank.  The following instructions will help you install this tank on all years of the XR650L or the 1988-2000 XR600Rmotorcycle.  There may be some plastic shavings left in the tank from the manufacturing process.  You can use compressed air to blow out the tank.  You may also want to rinse out the tank using a small amount of fuel before installing it. The instructions on the back side of this page will help you to install your new tank properly.  Please note that on the XR650L this tank will not use the factory

“Air Scoops”. We have sold this tank for years and have not had complaints about overheating or

any other problems from running this setup.

PLEASE SEE THE REVERSE SIDE OF THIS PAGE FOR INSTALLATION INSTRUCTION

INSTRUCTIONS FOR MOUNTING THIS TANK ON A XR650L MOTORCYCLE

1.) Begin by removing your old tank and petcock.  Drain your old tank in a well ventilated area.

2.)  Install the petcock from your old tank onto the new one by inserting it into the tank and carefully

threading it onto supplied petcock adapter.

3.) Remove the wire form “safety bar” from the Clarke tank and set it aside for later installation.

4.) Cut the padding provided into 2 pieces approximately 4” long and 2” wide.  You can use more if you choose.  The padding is supplied to provide more stability to the tank since there are no support pads as

is typical on most plastic tank applications.

5.) Zip-Tie or duct tape them to the front and rear section of the frame as shown in the diagram.

6.)  Now place the tank over the frame and push it forward into position on the rubber pucks that will slide into the plastic mounting brackets that are pre-installed on the tank.  Align the rear mount hole with it’s respective mount hole at the back of the tank/frame and using the supplied bolt fasten it firmly.

7)  Fish the wire form “safety bar” through the front part of the tank/frame area and fasten it to the tank

using the screws provided.

8.)  Route the fuel line over the canister and hook it from the carburetor to the petcock

and tighten the securing nut.

9.)  Turn the petcock to “OFF”.  Fill the tank with fuel and check for leaks.

10.) Re-install the seat and fasten the seat mount bolts securely make sure all bolts are tight and the

petcock is secure.

11.) You are now ready for riding. Enjoy your new Clarke tank.

INSTRUCTIONS FOR MOUNTING THIS TANK ON A 1988-2000 XR600R MOTORCYCLE

1.) Begin by removing your old tank and petcock.  Drain your old tank in a well ventilated area.

2.)  Install the petcock from your old tank onto the new one using your original hardware.

3.) Transfer your original front mounts, seat retaining screw and spacer to the new tank.

4.)  Slide the new tank onto the frame and align the front mounts with their mounting points.

Use 1 original front mount bolt on the left side ( Don’t forget the clutch cable wire form .)

On the right side use the supplied longer 6mm x 45mm bolt and aluminum spacer.  Now tighten down both

mounts to the frame.

5.) Route the fuel line over the canister and hook it from the carburetor to the petcock

Turn the petcock to “OFF”.  Fill the tank with fuel and check for leaks.

6.) Re-install the seat and fasten the seat mounts securely.  You are now ready for riding.

# Text boxes

PADS

FRAME