Clarke Manufacturing Inc. 13388 S. Molalla Forest Rd. Molalla OR. 97038

Part # 1452 XR50 OR CRF50 2000-2007

STOCK CAPACITY FUEL TANK

Thank you for purchasing a Clarke fuel tank.  The following instructions will help you install this tank on a XR50/CRF50 2000-2007 motorcycle. There may be some plastic shavings left in the tank from the manufacturing process.  You can use compressed air to blow out the tank.  You may also want to rinse out the tank using a small amount of fuel before installing it. The instructions on the back side of this page will help you to quickly install your new tank

PLEASE SEE THE REVERSE SIDE OF THIS PAGE FOR INSTALLATION INSTRUCTIONS

1.) Begin by removing your old tank, shrouds, rear fender/seat assembly and petcock.

Drain your old tank in a well ventilated area.

2.) Transfer your petcock to the new tank using your original hardware.

3.) Transfer the rear seat mount stud to the new tank.  The tank is now ready for installation.

4.) Set the tank on the frame and align the new included mounting bolts over their locations adjusting the rear slotted grommet as necessary.  Tighten the bolts down and reinstall the seat and rear fender assembly.

5.) Attach the inside of the shrouds using the new 6mm bolt, nut and washer setup.

6.) Go back and check all the bolts to make sure they are tight and hook up the fuel line to the petcock.

7.) Add fuel to the new tank and check for leaks.  If there are none then you are now ready to ride.