Clarke Manufacturing Inc. 13388 S. Molalla Forest Rd. Molalla OR. 97038

Part # 1458 CRF450R FOUR STROKES 2005-2008

2.8 GALLON FUEL TANK

Thank you for purchasing a Clarke fuel tank.  The following instructions will help you install this tank on a CRF450R 2005-2008 four stroke motorcycle.  There may be some plastic shavings left in the tank from the manufacturing process.  You can use compressed air to blow out the tank.  You may also want to rinse out the tank using a small amount of fuel before installing it. The instructions on the back side of this page will help you to quickly install your new tank.

PLEASE SEE THE REVERSE SIDE OF THIS PAGE FOR INSTALLATION INSTRUCTIONS

1.) Begin by removing your old tank, shrouds and petcock.  Drain your old tank in a well ventilated area.

2.) Install your original petcock mount in the new tank.

3.) Place the tank in the frame and align the front of the tank over the mount hole.

4.) Using the 6mm x 35mm bolt supplied and bolt the tank loosely to the front mount hole.

5.) Transfer the rear seat mount stud and the rear strap mount screw to the new tank.

6.) Attach the rubber strap to the rear screw.

7.) Using the original 5mm shroud bolts, loosely attach the upper part of the shrouds to their original positions.

8.) The lower section of the shrouds where they attach to the frame and radiator mounts will require you to

use the supplied 6mm x 35mm bolts and 1/4” washers with the supplied .500 spacer between the

frame/mount and back side of the shroud.  Install where shown in the diagram on the front of this page.

9.) Repeat this process for the right side shroud.

10.) Go back and tighten all bolts, hook up fuel line and fill with gas.

11.) Check for leaks.

12.) Re-install the seat and fasten the seat mount bolts securely.

13.) You are now ready for riding. Enjoy your new Clarke tank.

# Text boxes

Stock 5 mm Bolt

LEFT SHROUD

Stock 5 mm Bolt

6mm x 35mm Bolts

.250 Washers

.500 Spacers

Install Behind Shrouds