Clarke Manufacturing Inc. 13388 S. Molalla Forest Rd. Molalla OR. 97038

Part # 1414 1986-1988 KLF300 BAYOU

STOCK CAPACITY FUEL TANK

Thank you for purchasing a Clarke fuel tank.  This tank is intended for use on the 1986-1988 KLF300

Kawasaki Bayou.  There may be some plastic shavings left in the tank from the manufacturing process.  You can use compressed air to blow out the tank.  You may also want to rinse out the tank using a small amount of fuel before installing it.

1.) Shut off fuel supply and disconnect fuel line and remove the original tank and petcock.  Drain your old tank in a well ventilated area.

2.) Install your original petcock in the new tank.

3.) Slide the tank onto the front rubber mounting pucks.

4.) Use your original rear mount bolt to bolt the new tank tightly to the rear mount hole.

5.) Hook up the fuel line, turn the petcock to the OFF position and fill the tank with gas.

6.) Check for leaks.

7.) Now re-install the tank cover. The hole in the plastic tank cover will need to be enlarged to

accommodate the new larger fuel cap.  Using a sharp razor knife, carefully trim the hole and allow at

least a 1/4” of clearance to allow for expansion.

8.) Re-install the rear fender and seat assembly.

9.) You are now ready for riding. Enjoy your new Clarke tank.