Clarke Manufacturing Inc. 13388 S. Molalla Forest Rd. Molalla OR. 97038

Part #1441 SUZUKI LTZ400 OR KAWASAKI KFX400

STOCK CAPACITY FUEL TANK

Thank you for purchasing a Clarke fuel tank.  This tank is intended for use on a LTZ400 or KFX400.  There may be some plastic shavings left in the tank from the manufacturing process.  You can use compressed air to blow out the tank.  You may also want to rinse out the tank using a small amount of fuel before installing it.  Please note that for this tank to be mounted properly it will require that the top of the tank cover needs to be removed from the front fender assembly.  You will also have to cut off the unnecessary tabs that are located around the top of the tank area of the front fender assembly as shown in the picture below.  This can be easily achieved using a razor knife.  It is NOT necessary to cut off any other fender tabs or hooks to install this tank properly.

PLEASE SEE THE REVERSE SIDE OF THIS PAGE FOR INSTALLATION INSTRUCTIONS

1.)  Begin by rinsing out your new tank with a small amount of fuel.  Do this in a properly ventilated area.

2.)  Remove the seat and rear fender assembly.

3.)  Remove the reverse switch bracket.

4.)   Remove and loosen the front fender assembly bolts and push/pull tabs as needed to remove the side panel assemblies as well.  Leaving the front fender assembly in place but loose and rotated forward, carefully unbolt and remove your stock fuel tank.

5.)  You can now carefully cut off the tabs as shown in the picture on the front page that they are flush with the front fender assembly.

6.)  Drain the fuel from your stock tank in a well ventilated area.  Remove the stock petcock from your original tank and install it on the new tank using your original bolts and the new flat gasket that is provided.

7.)  Install your stock seat mount onto the rear of the tank.

8.)  Take the tank and carefully slide it forward into the front rubber mount until the rear rubber grommet

holes line up over the rear mount locations.  Using the new 6mm bolts and washers start one loosely and

then get the other one started.  Once both bolts are started, you can tighten down the rear of the tank.

9.)  Now re-install your fuel lines.  You can now fill the tank with fuel and check for leaks.

10.)  Carefully rotate the front fender assembly back into place and re-install the reverse switch.

11.)  You can now re-install the side panels and tighten all bolts and push/pull buttons.

12.)  Re-install the seat and rear fender assembly.  Go back and double check your work.

13.)  You are now ready for riding.  Enjoy your new Clarke tank!