Clarke Manufacturing Inc. 13388 S. Molalla Forest Rd. Molalla OR. 97038

Part # 1449 CRF250R and CRF250X FOUR STROKES 2004-2008

3.0 GALLON FUEL TANK

Thank you for purchasing a Clarke fuel tank.  The following instructions will help you install this tank on a CRF250R and X 2004-2008 four stroke motorcycle.  There may be some plastic shavings left in the tank from the manufacturing process.  You can use compressed air to blow out the tank.  You may also want to rinse out the tank using a small amount of fuel before installing it. This tank will fit without any modification on the CRF250R model but will require the use of the included front mount bracket if you are installing it on the CRF250X. The instructions on the back side of this page will help you to quickly install your new tank

PLEASE SEE THE REVERSE SIDE OF THIS PAGE FOR INSTALLATION INSTRUCTIONS

1.) Begin by removing your old tank, shrouds and petcock.  Drain your old tank in a well ventilated area.

2.) Install your original petcock in the new tank.

3.) Whether you have an “R” or an “X” model you will not need to use your stock front mount.

If you have the “R” model simply put the tank into the frame and bolt the tank down through the

grommet on the Clarke tank loosely and proceed to step 6.

4) If you have an “X” model:  take the supplied front mount bracket assembly and insert the aluminum spacer into the front grommet on the Clarke Tank.  Insert the carriage bolt in the bracket and push it up through the grommet and spacer so the threaded end is up.  Now, loosely attach the washer and lock nut to the bolt to keep it from coming out.

5.) Place the tank into the frame and push it into position aligning the bracket over the threaded hole

where your OE tank mount bolted to. If you have the “X” model, use the supplied tapered head screw to

loosely bolt the tank to the frame through the new bracket.

6.) Transfer the rear seat mount stud and the rear strap mount screw to the new tank.

7.) Install all shroud bolts loosely on the tank section using the original 5mm shroud bolts.

After locating the shrouds to the correct position, tighten shroud bolts. Repeat this process

on the opposite side.

8.) Go back and tighten the front mount bolt.

9.), Attach the rubber strap to the rear screw, hook up fuel line and fill with gas.

10.) Check for leaks.

11.) Re-install the seat and fasten the seat mount bolts securely.

12.) You are now ready for riding. Enjoy your new Clarke tank.