Clarke Manufacturing Inc. 13388 S. Molalla Forest Rd. Molalla OR. 97038

Part # 1383 ATC200X 1983-1985 ONLY

3.0 GALLON CAPACITY FUEL TANK

Thank you for purchasing a Clarke fuel tank.  This tank is intended for use on an ATC200X. There may be some plastic shavings left in the tank from the manufacturing process.  You can use compressed air to blow out the tank.  You may also want to rinse out the tank using a small amount of fuel before installing it.  Please Note:  This tank does not look like your original.  It also will not use the original factory air scoops.

PLEASE SEE THE REVERSE SIDE OF THIS PAGE FOR INSTALLATION INSTRUCTIONS

1.) Shut off fuel supply and disconnect the fuel line and remove the original tank and petcock.  Drain your old tank in a well ventilated area.

2.) Remove the safety bar from inside the tank and set it aside for final installation.

3.) Install your original petcock to the new tank carefully threading it onto the supplied aluminum petcock adapter.

4.) Slide the tank onto the front rubber mounting pucks.

5.) Use supplied rubber strap and pull it down over the clip to attach the rear of the tank to the frame.

6.) Take the safety bar and slide it across and under the front part of the frame and using the supplied

phillips head screws, affix the safety bar to the tank on both sides.  The safety bar is simply an extra precaution to keep the tank from lifting off of the frame.

7.) Now hook up the fuel line, turn the petcock to the OFF position and fill the tank with gas.

8.) Check for leaks.

9.) Re-install the rear fender and seat assembly.

10.) You are now ready for riding. Enjoy your new Clarke tank.